## Slide 1: A Unified Approach for ALTO Properties (no draft yet)
Wendy Roome
Alcatel-Lucent/Bell Labs (NJ)
IETF 92
March 26, 2015

## Slide 2: Motivation
In the beginning there were Endpoint Properties (EPs).
EPs were independent of the Network Map, but there was only one Network Map, so it was moot.
And then we added multiple Network Maps, and “resource-specific” EPs vs. “global” EPs, and EPs became more complicated.
And then we proposed PID Properties.
And Abstract Network Element Properties (topology draft).
And Foo Properties, and Bar Properties, and ….
Let’s unify all those Property Services into a common framework that can be extended for new entity classes

## Slide 3: Entity Naming
Extend typed endpoint addresses:
entity-name := entity-class : entity-specific-name
entity-class := ipv4 | ipv6
cidrv4 | cidrv6 |
mac48 |
pid |
ane | ….
Examples:
ipv4:1.2.3.4
cidrv4:1.2.0.0/16
pid:mypid1
ane:link42
ane:datacenter-14.rack-37.tor-router

## Slide 4: Property Naming
Common property name space, independent of entity type
  Values should have same format for all entity types
  Interpretation may vary, but basic meaning should be the same
  If a property does not make sense for an entity type, skip it!
Good example:
  geo-location property is “latitude longitude [height]”
  For PIDs, it’s the centroid of endpoints in PID
Bad example:
  For endpoints, geo-location is “lat long [height]”
  For PIDs, geo-location is “nw-lat nw-long se-lat se-long”
Only applies to IANA registered properties. For “priv:” properties, do whatever you want.

## Slide 5: Property Map Services
Two new services, modeled on Full & Filtered Network Maps:
  GET-mode Full Property Map
  POST-mode Filtered Property Map
IRD gives property names and entity types each map returns
  Implicit cross product of entity types & property names
  Server omits meaningless combinations
  Server can define multiple maps to avoid meaningless combinations
A Full Property Map for Endpoint Properties???
  Yes, there are billions of endpoints, but the server might only define properties for a few thousand
  And if a Full Map would be too big, provide a Filtered Map instead

## Slide 6: Property Maps & Network Maps
In RFC 7285, Endpoint Properties were independent of Network Maps
  Holdover from early single Network Map versions of the protocol
  Illusion, because the “pid” property depends on the Network Map
  Led to “resource-specific property” kludge (mea culpa!)
Conceptual change:
Each Property Map resource depends on one Network Map
Many entity types are defined by the Network Map, so this provides necessary context
Use the default Network Map for any properties that really are independent of the network

## Slide 7: IRD Entries: Full Property Maps
"full-property-1" : {
"uri" : "http://----------",
"media-type" : "application/alto-propmap+json", (new type)
"uses" : "my-default-network-map",
"capabilities" : {
"prop-types" : [ "geo-location", "asn" ],
"entity-types" : [ "pid" ]
}
},
"full-property-2" : {
"uri" : "http://----------",
"media-type" : "application/alto-propmap+json",
"uses" : "my-default-network-map",
"capabilities" : {
"prop-types" : [ "bandwidth", "type" ],
"entity-types" : [ "ane" ]
}
}

## Slide 8: IRD Entries: Filtered Property Maps
"filtered-property-1" : {
"uri" : "http://----------",
"media-type" : "application/alto-propmap+json",
"accepts" : "application/alto-propmapfilter+json", (new type)
"uses" : "my-default-network-map",
"capabilities" : {
"prop-types" : [ "pid", "location", "asn" ]
"entity-types" : [ "ipv4", "ipv6", "pid" ]
},
},
"filtered-property-2" : {
"uri" : "http://----------",
"media-type" : "application/alto-propmap+json",
"accepts" : "application/alto-propmapfilter+json",
"uses" : "my-default-network-map",
"capabilities" : {
"prop-types" : [ "bandwidth", "type" ]
"entity-types" : [ "ane" ]
},
}

## Slide 9: Filtered Request
Client gives property names & entity names:
POST /---- HTTP/1.1
Host: alto.example.com
Content-Length: ###
Content-Type: application/alto-propmapfilter+json
Accept: application/alto-propmap+json,application/alto-error+json
{
"properties" : [ "geo-location", "asn" ],
"entities" : [ "ipv4:1.2.3.4", "pid:mypid2" ]
}

## Slide 10: Response
Similar to current Endpoint Property service:
HTTP/1.1 200 OK
Content-Length: ###
Content-Type: application/alto-propmap+json
{
"meta" : {
"dependent-vtags" : [
{"resource-id": "my-default-network-map",
"tag": "7915dc0290c2705481c491a2b4ffbec482b3cf62"
}
]
},
"property-map": {
"ipv4:1.2.3.4" : { "geo-location": "40.1205,-74.2519",
"asn": 65000 }
"pid:mypid2" : { "geo-location": "40.0,-74.0",
"asn": 65000 }
}

## Slide 11: ALTO Properties Simplify Access To …
DNS:
Properties for (say) “dns:ietf.org”:
  “address” is preferred address
  “addresses” is list of alternate addresses
  Properties for the various DNS resource records?
  Resolved at ALTO server
WHOIS:
Properties for (say) “whois:ietf.org”:
  “registrant”, “admin” and “tech” could be JSON dictionaries
  “name-servers” could be list of registered name servers

## Slide 12: Effect On Current Documents
RFC 7285:
Deprecate the current Endpoint Property Service
Do not define any new resource-specific properties
PID Properties Draft:
Extend this Property Map service
Define the “pid” and “cidr” entity types
Define inheritance between pids, cidrs and endpoints
New Properties Drafts:
Define the entity types for those properties

## Slide 13: What Next?
Do you like this approach?
If so, write draft & circulate via mailing list